## Slide 1
Photonics Research Lab.
Department of Electronic Engineering
Kwangwoon University
Om Raj Sapkota
September 05, 2019
Replication of Thermal tuners on a silicon nitride platform

## Slide 2: Replication of previous works
Purpose: We would like to replicate the temperature gradient result of the previous paper
Ref. https://arxiv.org/abs/1604.02958
D. Perez., ‘Thermal tuners on a silicon nitride platform,’ arXiv , 2016

## Slide 3: Structure and parameter
Item | Value | Unit | Description
TSiO2 | 3.5 | um | Thickness of SiO2
Tau | 100 | nm | Thickness of Au
Tcr | 30 | nm | Thickness of Cr
We | 5 | um | Width of electrode
TSiN | 300 | nm | Thickness of SiN
WSiN | 1 | um | Width of SiN
Tbox | 2 | um | Thickness of BOX
Tele | 130 | nm | Tau+Tcr
Electrode (Au and Cr)
We
WSiN
TSiN
Tbox
Tele
Schematic diagram
Table of parameters
Si substrate
TSiO2
SiN
BOX (SiO2)
Air
We designed the structure by using parameters written on the paper

## Slide 4: Comparison of contour map of temperature ) Expected vs. Calculated
Expected result
Calculated result from COMSOL
 | Min. Temperature | Max. Temperature
Expected | 12 | 102
Calculated | 25 | 25.08
Totally different
To apply the power (297.32 mW) to the electrode, we used the physics called ‘Heat transfer in solids. (For the details, please refer to next slide)
But, the result is totally different from the expected result of the paper.
No change
Temperature [°C]

## Slide 5: Used physics – Heat transfer in solids
We used electrode as a heat source and applied the power (297.62 mW) to the electrode (Au and Cr)
SiN
SiO2
Electrode (Au and Cr)
Air
Si
The temperature at this boundary is set to T = 25 °C

## Slide 6: Comparison: Temperature range (Expected vs. Calculated)
If we changed the P0 of ‘Heat Source’ from 297.32 mW to 275.45 W, we could see some changes in the result
 | Min. Temperature | Max. Temperature
Expected | 12 | 102
Calculated | 27.66 | 102
Expected result
Calculated result from COMSOL
P = 297.62 mW
P0: 297.32 mW  275.45 W
Change
Temperature [°C]

## Slide 7: Question
From the calculated result, it looks we approached a wrong way to replicate the paper result. Is this right way to use physics ‘Heat Transfer in solids’?
Which physics do you suggest for this situation? If so, please let us know any example to understand that physics?