## Slide 1
Using Artificial Intelligence (AI) within COMSOL Multiphysics® to Create Machine Learning Tools
COMSOL European Conference:
Florence, 22-24 October 2024
F. Viry1, M. Sturma2, P. Namy1, B. Barbet2
1 : SIMTEC, 5 rue Felix Poulat 38000 Grenoble France
2 : MARKEM-IMAJE, Bourg-lès-Valence, France
Property of SIMTEC - All rights reserved
Notes: Hello everybody, my name is XXX, and I’m going to talk to you today about modeling of the YYYusing Comsol Multiphysics.
This work has been performed in collaboration between XXX (an international leader in XXX) and Simtec, the leader of the French Comsol Certified Consultant and a key partner of the COMSOL Certified Consultant Worldwide.

## Slide 2
Outline
  Background – Motivations – Objectives
  Modelling and Numerical Model
  Main Results
  Conclusions – Perspectives

## Slide 3
French Numerical modelling consultancy
Leader in France of the COMSOL Certified Consultants, key partner worldwide
9 members Eng.D. + Ph.D.
Main partners:
  big international companies
  laboratories
Involved in the Research projects like EU FP (SHARK, SisAl)/ PhD supervision
Before starting, who we are… www.simtecsolution.fr
SIMTEC : Fundamentals
Notes: FP= framework program Two words about SIMTEC and our clients.
Simtec is the leader of the French COMSOL certified consultant company.
There are 7 members and we all have an engineering degree and a PhD. That means we have an extensive research background and we can handle very complex problems in a range of physics area and industry sectors.
Our main clients are big groups and government laboratories. You can see here some of them
We are also involved in research, for instance we are part of European Research Projects like SisAl Pilot.
So can go to our website to discover more user cases!

## Slide 4
I. Background – Motivations – Objectives
At SIMTEC,
Creation of dozen of COMSOL model every year
Worldwide,
A big boom in AI assisted processes
(chatgpt, deepl…)
?

## Slide 5
I. Background – Motivations – Objectives
Collaboration with MARKEM-IMAJE
Continuous Inkjet printing (CIJ) : high speed printing for marking and coding
How does CIJ work?
  High speed emission of droplets ( at )
  Charge of particular droplets ()
  Deflection of charged droplets in an electric field ()
  Impact of charged droplets on the printed support
Goal: maximizing printing quality
Printing quality depends on:
  Breakoff quality at generation
  Deflection
  Interactions during flight
Deflection electrode 2
Deflection electrode 1
Charge electrodes
Droplet generator
Gutter
Nozzle
Printed support
Trajectory of a non-charged droplet
Trajectory of a charged droplet
Schematic representation of a print head

## Slide 6
II. Modelling and Numerical Model
Tools
Data treatments
Training models
 Data generation/collection

## Slide 7
II. Modelling and Numerical Model
Collecting Data
Choose a set input values (design of experiment)
Build the “input matrix” in the Python code
Perform one simulation per input value (COMSOL)
For each simulation: export the output as a TXT file (COMSOL)
Project outputs into a common subspace (COMSOL or Python)
Build the “output matrix” in the Python code
Use-case
2D phase function
(COMSOL)
1D point cloud of the border (COMSOL)
Ink viscosity
Droplet shapes
Projection on a common grid (Python)

## Slide 8
II. Modelling and Numerical Model
Training a Model (Python)
Choose a mathematical model to express the viscosity according the radius of the droplet
Choose an optimization criterion to train the model
Regularization to avoid overfitting
Use-case
Linear model:
Input prediction
Output
Parameters of the mathematical model to optimize
Optimization criterion: minimization of the MSE
To minimize
Regularization: LASSO
To choose appropriately to prevent overfitting
Notes: The model is often “too complex”, and the optimization criterion may include regularization to prevent overfitting

## Slide 9
III. Main Results
Dataset: droplets shapes at break simulated for multiple values of viscosities (in cP)

## Slide 10
III. Main Results
Train set
Expected
Predicted
Good fit on train set
Bad predictions on test set
 Overfitting X

## Slide 11
III. Main Results
Train set
Expected
Predicted
Bad fit on train set
Bad predictions on test set
 Underfitting X

## Slide 12
III. Main Results
Train set
Expected
Predicted
Good fit on train set
Good predictions on test set
 Good model ✓

## Slide 13
IV. Conclusions - Perspectives
Interest of Machine Learning methods:
  Minimize the simulation computational cost  Building Surrogate Models
  Retrieve simulation inputs providing a given output  Solving Inverse Problems
What we have done:
  Extract inputs/outputs data from COMSOL
  Solve an inverse problem using Supervised Machine Learning tools in Python
Flexibility of COMSOL is of great help to do so 
Coupling COMSOL with Machine Learning tools is feasible!

## Slide 14
To finish…
Thank you!
Q&A?
Our question: Who would like to try on your models? 
Patrick NAMY
SIMTEC (+33) (0)9 53 51 45 60
patrick.namy@simtecsolution.fr