## Slide 1: Simulating the Coupled Mass and Heat Transport in Package Material during Induction Sealing
Henrik Makungu Askfelt, Giovanni Betti Beneventi
COMSOL Conference - Florence, Italy, 22 October 2024

## Slide 2: Outline
Introduction
  Tetra Pak, Tetra Pak® Package Material, Induction Sealing
Package material model: heat and mass transport
Induction heating device model
Results & discussion

## Slide 3: Outline
Introduction
  Tetra Pak, Tetra Pak® Package Material, Induction Sealing
Package material model: heat and mass transport
Induction heating device model
Results & discussion

## Slide 4: Tetra Pak A world leading food processing and packaging company
Packaging technology: design and engineering of Filling Machines
Automated machines; from package material reels to liquid food containers in the order of thousands-per-hour
Stored food must stay fresh and safe for consumption for 1 year without the need for preservatives or refrigeration
> 8k Filling Machines in operation
Tetra Pak® packages produced 2023

## Slide 5: Filling machines, package material, induction sealing
Paperboard: Porous, Hygroscopic
Package Material: multi-layered
Sterilization, Forming, Filling, Sealing, Cutting
Next
How is induction heating of package material affected by board properties?
Induction sealing is deeply impacted by paperboard physics
Heating  Drying  Energy
Heating  Vapour  Pressure
Induction sealing process
Exploit high electrical conductivity of Al-foil
(eddy current) to heat-up the polyethylene
for polymer welding.
Typically: up to 150 ℃ in < 1 s.

## Slide 6: Outline
Introduction
  Tetra Pak, Tetra Pak® Package Material, Induction Sealing
Package material model: heat and mass transport
Induction heating device model
Results & discussion

## Slide 7: Package material model: heat and mass transport
Paperboard heat & mass transport – Mixture theory [2]
Al-foil heat transport
Mass Balance
Mass Balance
Mass Balance
Energy Balance
Polymers heat transport
Energy Balance
Energy Balance
 |  | 0 | 
 |  | 0 | 
[2] H. Askfelt and M. Ristinmaa, "Experimental and numerical analysis of adhesion failure in moist packaging material during excessive heating," International Journal of Heat and Mass Transfer, vol. 108, pp. 2566 - 2580, 2017
from

## Slide 8: Outline
Introduction
  Tetra Pak, Tetra Pak® Package Material, Induction Sealing
Package material model: heat and mass transport
Induction heating device model
Results & discussion

## Slide 9: Induction heating device model (2-D)
Test setup [1]
[1] M. Giangolini, G. Betti Beneventi and A. Babini, "Assessment of thermographic tools for the validation of physics-based models of an induction sealing process," International Journal of Applied Electromagnetics and Mechanics, vol. 75, no. 2, pp. 179-191, 2024.
Coil excitation – Current
 Total load power fixed
Coil excitation – Current
Laminate
Outside
Inside
Paperboard
Al-foil
Active area
Tape
Package Material
Cross - section
Return area
aluminum coil
ac current (f ~ 500 kHz)

## Slide 10: Induction heating device model (2-D)
Colorbar: norm(B) [mT]
Contour lines: Az []
Normalized electromagnetic surface loss. density vs. coordinate
Next: sensitivity analysis vs. board initial moisture ratio and density
  Excitation: load power (~650 W) ; 600 ms of on-time (Frequency –Transient)

## Slide 11: Outline
Introduction
  Tetra Pak, Tetra Pak® Package Material, Induction Sealing
Package material model: heat and mass transport
Induction heating device model
Results & discussion

## Slide 12: Model results - Sensitivity analysis
Parametric sweep
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
Maximum of drying and internal pressure over paperboard domain
Evolution of the maximum temperature of the package material inside top surface
initial
board density
initial moisture ratio
Time-evolution at the board/laminate interface, above the coil active area

## Slide 13: Discussion - Model vs. experimental data carried out on a given board grade
Matching between model and data [1] currently is not satisfactory
Prediction improved with temperature-dependent heat transport parameters of PE
The model can be used in its present state for relative comparisons and to study interplay of physical parameters
COMSOL Multiphysics® as enabling technology to allow the collaboration of modeling engineers having different expertise (e.g., paperboard physics / electromagnetic modeling)
FLIR cooled camera
Max. temperature on inside top surface vs. time
[1] M. Giangolini, G. Betti Beneventi and A. Babini, "Assessment of thermographic tools for the validation of physics-based models of an induction sealing process," International Journal of Applied Electromagnetics and Mechanics, vol. 75, no. 2, pp. 179-191, 2024.

## Slide 14: Recap
With COMSOL we are able to simulate the package material response during induction heating.
The model is able to capture complex multiphysical couplings such as gauge pressure build up and drying
The model may be used to understand how different attributes of the board will affect the package material behavior
Improve polymer model
- Heat transport & phase transformation
Key takeaways
Next step

## Slide 15: Backup Slides

## Slide 16: Tetra Pak - World leading food processing and packaging solutions company
Processing
Solutions and equipment for dairy, plant-based, cheese, powder, ice cream, beverages and prepared food.
Packaging
A complete carton packaging range for consuming food products offering convenience, easy opening, optimal shelf life and the ability to give maximum brand exposure.
Services
Helps improve performance, optimise costs and ensure food safety throughout the lifecycle of operations.

## Slide 17: Introduction - Tetra Pak Packaging
Our Ambition
To deliver the world's most sustainable food package.
https://www.tetrapak.com/sv-se/about-tetra-pak/who-we-are/facts-figures
Tetra Pak® packages sold 2023
8.5 k Filling machines in operation
Simulation driven design
Necessary tool when approaching our Ambition

## Slide 18: Model Results - Sensitivity analysis
Parametric sweep
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
  Lower PE temperature for higher density board
    higher specific heat
    higher thermal conductivity
  Lower PE temperature the higher the moisture content
    higher specific heat
    higher thermal conductivity
    more energy required to dry
initial density
initial moisture ratio
PE = polyethylene
Max. temperature on inside top surface vs. time

## Slide 19: Model Results - Sensitivity analysis
  located on top left corner of board below Al-foil nearby active area
  higher for higher initial moisture ratio  more desorption
    increased driving force for drying
  higher for decreased density  increased gas volume
    gas accumulates more water
    ease for vapor to flow within the board
  higher initial moisture  more desorption
  increased density  less desorption
    increase resistance for gas to flow higher pressure  higher desorption
    BUT
    increased density  lower temperature  lower pressure  lower desorption
  decreased temperature dominates over higher mass flux resistivity
Parametric sweep
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
initial density
initial moisture ratio
Max drying over paperboard domain (end of heating phase)
Max internal pressure build-up over paperboard domain (end of heating phase)

## Slide 20: Model Results - Sensitivity analysis
Drying and internal pressure time evolution at the board/laminate interface, above the active area coil
Parametric sweep
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
Parameter | Value list | Unit
 | 0.04, 0.07, 0.1 | 1
 | 500, 700, 900 | 
initial density
initial moisture ratio