## Slide 1: Optimizing electrochemical conversion of CO2 to C2 products via multi-physics simulations
Dr. Aviral Rajora, Dr. Simone Dussi, Endino Gieske

## Slide 2: About TNO
TNO: Netherlands Organization for Applied Scientific Research
  >4200 employees, several locations in the Netherlands
  Independent not-for-profit organization for research in between academia and industry
  From public-private collaborative projects (NL, EU) to contract research
  Six main research units
Energy & Materials Transition unit
  R&D division focusing on industrial processes
From 2015 VOLTACHEM Program for accelerating industrial electrification
Helmond
Geleen
Bergen op Zoom
Groningen
Petten
Amsterdam
Leiden
The Hague
Rijswijk
Delft
Eindhoven
Utrecht
Zeist
Soesterberg
          Locations
          Lab facilities
https://www.voltachem.com/
TNO, 2024. All rights Reserved.

## Slide 3: Multi-scale Electrochemical Flow Modelling
TNO, 2024. All rights Reserved.
Water electrolyser
Science 349, 1529 (2015)
CO2 electrolyser
Redox Flow Battery

## Slide 4: There are a lot of different configurations
TNO, 2024. All rights Reserved.
Current TNO focus: one-gap flow cell or membrane-electrode-assembly (MEA) with zero-gap, using AEM

## Slide 5
Multi-physics modelling to guide cell design
TNO, 2024. All rights Reserved.
  Models needed to quickly screen different designs and operating conditions
  1D models developed based on pioneering works of Weng, Bell, Weber and recent study of Ehlinger et al.
  Steady-state and isothermal simulations of coupled phenomena at cell-level:
  Flow
    Darcy’s law, simplified 2-phase using saturation curves
  Species transport (12 species)
    Gaseous species transport using multicomponent diffusion
    Aqueous species using Nernst-Planck
    Donnan potential included in transport across AEM for MEA configuration
  Reactions (7+5 heterogeneous + homogeneous)
Outputs: I-V curve, Faraday efficiency, spatial distributions of key quantities
Ehlinger et al., ChemElectroChem 11 (2024)
  Weng, Bell, Weber PCCP (2018),
  En. Env. Sci. (2019), En. Env. Sci. (2020)

## Slide 6
1D MEA model
TNO, 2024. All rights Reserved.
Tertiary Current Distribution
  Porous Electrode: DM,MPL,CL
  Porous Electrode Reactions: CL
  Ion Exchange Membrane: Membrane
CO2R
Homogeneous reactions
Law of mass action
OER
HER
Butler-Volmer or Tafel kinetics

## Slide 7
1D MEA model
TNO, 2024. All rights Reserved.
Tertiary Current Distribution
  Porous Electrode: DM,MPL,CL
  Porous Electrode Reactions: CL
  Ion Exchange Membrane: Membrane
Transport of Concentrated Species in Porous Media
  Cathode DM, MPL, CL
Darcy’s law
  Cathode DM, MPL, CL

## Slide 8: Boundary conditions
Physics
Gas channel | Cathode Diffusion Medium:
  P = 1 atm
  ωCO2 = 0.94, ωH2O = 0.04, ωH2 = 0.01, ωCO = 0.01
  φs = 0 V
Microporous Layer | Cathode Catalyst Layer:
  Jaq = 0
Cathode Catalyst Layer | Membrane:
  Jgas = 0
Anode Diffusion Medium | Anolyte:
  ci = cequi
  φs = φapplied

## Slide 9
Modelling electrode flooding
TNO, 2024. All rights Reserved.
S = 1, flooded case
0 < S < 1, wetted case
S = 0, dry case
S: pore saturation
Multiphase flow in porous media
Simplified to parameter S
Weng et al. (2018)
It depends on local conditions
Capillary pressure =
Zenyuk et al. (2015)

## Slide 10: Model validation (for CO2 to CO)
TNO, 2024. All rights Reserved.
    We thank Victoria Ehlinger for useful correspondence
Focus on gas-liquid behavior in cathode
Accurate saturation curves crucial to capture decrease in Faradaic efficiency
Several complex coupled phenomena: implementation details matter!
Porous layer
Catalyst layer
CO2 (g)
CO2 (aq)
CO2 dissolution in CL described as source term

## Slide 11
Include additional reactions to C2+ products
Good agreement with previous literature (for “ideal” wetting of S=0.64)
Extending the model to ethylene

## Slide 12
1D simulation results: gas-liquid management
TNO, 2024. All rights Reserved.
Impact of (average) saturation level of the different cathode layers on Faradaic efficiency
  GDL has minor impact
  Flooding of MPL can also be detrimental
  Catalyst layer is the most important one
cathode

## Slide 13
Much less done in literature for 2D, especially for CO2 to C2H4
  Few studies on planar electrodes, microfluidic and GDE flow cells
2D simulations to understand limitations to single-pass conversion
  Blake et al. shown limitations in 1m-long CO2->CO GDE flow cell, related to inhomogeneities in catalyst local environment
2D simulations to optimize catalyst distribution
  Segmented GDE: two types of catalysts (silver + copper) to promote in-situ tandem reaction (CO2->CO->C2H4)
  What about non-uniform catalyst distribution?
TNO, 2024. All rights Reserved.
Zhang et al., Nat. Catal., 5, 201, (2022)
Blake et al., ACS Sust. Chem. Eng., 11, 2840, (2023)
Qiu et al., Env. Chem. Lett. (2023), Yang et al. ACS Sus. Chem. Eng. (2020), Kas et al. ACS Sus. Chem. Eng. (2021)
2D simulations to address upscaling challenges

## Slide 14
  Upto 10 cm long channel simulated
  High current density (300 mA/cm2)
  For long channels, large mass fraction gradients seen in the simulation snapshot
  Performance is influenced due to inhomogeneity.
(ongoing) 2D simulations: counteracting inhomogeneities
Shown mass fractions in gas channel (3mm wide)
CO2
CO
C2H4
H2
CO2
CO
C2H4
H2

## Slide 15
(ongoing) 2D simulations: tuning catalyst loading
TNO, 2024. All rights Reserved.
Depending on manufacturing process, changes in catalyst loading can affect catalyst layer porosity, thickness, active surface area…
For a 10cm cell, decreasing (uniform) catalyst loading can improve performance

## Slide 16
CONCLUSIONS
TNO, 2024. All rights Reserved.
We model different electrolyzer configurations: MEA and one gap configuration
Catalyst loading can be tuned to improve performance
Catalyst layer design is crucial for performance of CO2 electrolyzer
There are large inhomogeneties in long electrolyzers
MPL could also be detrimental
For more info, collaborations, internships/vacancies:
aviral.rajora@tno.nl
Thank you for your attention!