## Slide 1: Implementing a new type of boundary condition using the COMSOL Physics Builder
Michael Kröhn, GRS
22nd October, 2024
COMSOL Conference, Florence

## Slide 2: Introduction
Swedish deposition concept: KBS-3
  Excavation of the deposition tunnel
  Drilling of the deposition boreholes
  Installation of bentonite blocks and waste cannisters
  Filling of the deposition tunnel
Planned development:
  Waterflow through fractures towards the cannisters

## Slide 3: Introduction

## Slide 4: Experimental set-up
0,01 ml/h
⌀50mm
41.6 mm
Bentonite sample
Compacted from granular material
target density (air dry): 1450kg/m³
initial water content: ~12.74 %
Syringe pump
  pump rate: 0.01 – 99.99 ml/h
  accuracy: 2.5 % (for intervals > 1 h and pump rates > 2 ml)
  obstruction alarm at 0.3 bar

## Slide 5: Workflow for creating an own COMSOL Interface
Implementation in COMSOL Physics Builder
Comparison with non-isothermal experiment data
Coupling with Heat Transfer in Porous Media Interface
Adding Neumann boundary condition
1
2
3
4
5
Theory

## Slide 6: COMSOL Physics Builder

## Slide 7: COMSOL model geometry
Boundary condition: no flow
Boundary condition: Neumann condition
Inflow between 1,41*10-6 and 7,07*10-6 kg/m²s

## Slide 8: Comparison of measurement and simulation results
1 Week
2 Weeks
3 Weeks
4 Weeks
6 Weeks
length [mm]
watercontent

## Slide 9: Conclusions
Results:
Successful implementation of Neumann boundary condition
Promising first simulations
Whats next:
Checking against other test scenarios
Advancing simulation capabilities
  Switching from Neumann to Dirichlet condition when full saturation is reached at the boundary
  Adapt the diffusion coefficient of the interlayer according to the water content

## Slide 10: Thanks for your attention