## Slide 1: Investigation for thermal analysis in COMSOL for fused filament fabrication
Robrecht Abts1, Jie Zhang1, Ming Wu 1,2, Mathias Verbeke2 , Eleonora Ferraris1
1 Department of Mechanical Engineering, KU Leuven, 3000 Leuven, Belgium
2 Department of Computer Science, KU Leuven, 3000 Leuven, Belgium
robrecht.abts@kuleuven.be

## Slide 2: Fused Filament Fabrication (FFF)
Feedstock
Build plate
Feed rollers
Cold end
Hot end
Nozzle
Working principle of the Fused Filament Fabrication technology

## Slide 3: Importance of build temperature in FFF
Diffusion at the interface
Temperature criterion for the (glass) phase transition ( T > Tc)
Cooling pattern during printing is essential
Evolution of bond formation: (1) neck formation (2) neck growth (3) diffusion at interface

## Slide 4: Importance of build temperature in FFF
Coupled-Multiphysics
polymer melt flow
heat transfer
phase change
10 times longer
Layer thickness
Comparison of printing speed influence on temperature and print quality
Notes: This slide can give you some inspiration to expalin the role of temp in FFF

## Slide 5: T4F3 simulation code
Types of energy transportation between elements
Interface T4F3-software to calculate temporal temperature

## Slide 6: Validation methodology
Overview of working method used in this study to compare T4F3 with COMSOL

## Slide 7: MATLAB implementation
for z = z_list
for y_index = 1:length(y_list)
for x = x_list
dist = sqrt((data.X(end)-x)^2+((data.Y(end)-y)^2));
time = time + dist / printingSpeed;
new_row = {time, x, y, z};
data(row_counter, :) = new_row;
row_counter = row_counter + 1;
end
end
end
t(s) x y x
0 0 0.2 0.25
1.4 18 0.2 0.25
1.5 18 0.6 0.25
2.9 0 0.6 0.25
3 0 0.2 0.75
4.4 18 0.2 0.75
4.5 18 0.6 0.75
5.9 0 0.6 0.75
6 0 0.2 1.25
7.4 18 0.2 1.25
7.5 18 0.6 1.25
8.9 0 0.6 1.25
0 0.2 1.75
Input
MATLAB-code
Output

## Slide 8: COMSOL implementation
Interpolation & Activation | Heat transfer module | Mesh
If (abs(x-x1(t))<= x_length/4 && abs(y-y1(t))<= Strand_width/2 && abs(z-z1(t))<= Layer_heigth/2 ,1,0) | Solid: Thermal cond., density, heat capacity  user defined If(solid.isactive, PLA, Air) Temperature: Build plate temperature Heat source: Go to Tnozzle at activation function location Heat flux: Convection at boundary | Cubic mesh Mesh size: Y: Size of strand Z: Layer heigth/4

## Slide 9: Preliminary results
Simulation settings
4x4x6 mm cube
Printing speed 5 mm/s
PLA print material
Tnozzle = 200°C
Tbuild plate = 60°C
Troom = 20°C

## Slide 10: Preliminary results: Comparison to T4F3
B
B
B
A
C
A: Different temperature peaks
  Data collection method
  Source temperature difference
  Cooling rate difference
B: Time shifts
  Different path generation
C: Similar effect next layers
  More analysis of patterns is needed

## Slide 11: Conclusion
New insights
Workflow for use of COMSOL in FFF thermal simulation
Conversion from T4F3 results
Future work
Improve current model (accuracy and calculating efficiency)
Make step towards free-form simulations

## Slide 12: Thank you! robrecht.abts@kuleuven.be

## Slide 13: References
[1] Bellehumeur, C., Li, L., Sun, Q., & Gu, P. (2004). Modeling of Bond Formation Between Polymer Filaments in the Fused Deposition Modeling Process. Journal of Manufacturing Processes, 6(2), 170–178. https://doi.org/10.1016/S1526-6125(04)70071-7
[2] J. Zhang, B. Van Hooreweder, and E. Ferraris, “T4F3: temperature for fused filament fabrication,” Progress in Additive Manufacturing, vol. 7, no. 5, pp. 971–991, Oct. 2022, doi: 10.1007/S40964-022-00271-0/FIGURES/15.