## Slide 1: Fluid Dynamic Modeling in Oven Chambers: Balancing Accuracy and Computational Efficiency
Comsol Conference
Florence, October, 2024
Ph.D, Christian Bianchi

## Slide 2: Main goal of the investigation
Reduction of computational complexity by choosing the best model strategy to simulate the fluid dynamics in a closed oven chamber
Optimization of the process workflow to maximize the efficiency of module usage

## Slide 3: Basic Hypothesis
The classical way to investigate the forced ventilation and thermal distribution in a closed chamber is to simulate the coupled CFD and HT problem in the full domain
A simpler, but less accurate way to make the same investigation is to separate the study of the driving force (fan) from the effect in the remaining chamber.
How good this accuracy can be?

## Slide 4: General concept
CFD + HT
Complex domain
CFD
Pipe & Distibutor domain
1
2
HT
Chamber domain
pipe
distributor
radial fan
Complex fan
chamber
Cylindrical velocity profile and pressure
chamber
STEP 1
STEP 2
STEP 3

## Slide 5: Steps
The analysis is characterized by three steps:
Step 1
Need of both CFD and HT modules for the entire simulation time over a complex domain
Step 2
Need of only the CFD module for a simplified domain
Step 3
Need of the only HT module for the chamber domain (complexity of the fan is excluded)

## Slide 6: Module usage and timing
CFD
HT
CFD
HT
STEP 2
STEP 1
STEP 3
Time
It can take longer if multiple angular position
must be assessed for full rotation (the lower the number of blades, the higher the impact)

## Slide 7: Step 1 – Model characteristics
physics setting
Two frozen rotors are defined
Gravity is also included
Pressure reference is set at one corner
Temperature is set at the resistors surface (500 degC), thermal dissipation can occur at the door

## Slide 8: Results - Step 1 – Full oven simulation
Full domain with fan, carter, resistors and cavity
Mag(U) (m/s)
Fluido weakly compressible
Turbolence model: k-ε
ω = 2000 rpm
PRESSURE POINT CONSTRAIN: pstat = 0 Pa
OVEN WALLS: wall + thermal insulator
OVEN DOOR: wall + thermal dissipation
RESISTORS: wall + thermal source
FANS: wall

## Slide 9: Step 2 – Model characteristics
Frozen rotor
Inlet pressure
Domain setting
Thin faces used to define the fan geometry
Outlet pressure

## Slide 10: Step 2 – simplified domain
Condotto di aspirazione + outlet indefinito.
Mag(U) (m/s)
INLET: ptotale = 0 Pa
OUTLET: pstat = 0 Pa
OUTLET_WALL: wall
*OUTLET (free flow) and OUTLET_WALL (stopped flow) are considered in the same ratio as in the real oven, given to the following value Aoutlet / Aoutlet_wall = 0,6470
Fan and walls: wall condition
Incompressible fluid
Turbolence model: k-ε
ω = 1000 rpm;
1600 rpm;
2000 rpm (fig);
2600 rpm

## Slide 11: Step 2 – Output quantities
Mag(U) (m/s)
p (Pa)
Vector velocity profile around external surface of the cylinder
Static pressure at the suction section of the fan
These two output profiles of step 1 are the input for step 3

## Slide 12: Step 2 – Experimental validation
The door of the oven was open to let the insertion of the pipe. The pipe was placed in front of the fan. A digital anemometer was used to measure the volumetric flow rate.
anemometro digitale
forno
v
ventola
Condotto aspirazione D=250mm , L=3m
Rpm | ṁ experimental (kg/s) | ṁ simulation (kg/s) | shift (%)
1000 | 0,163 | 0,153 | 6,22
1600 | 0,248 | 0,247 | 0,25
2000 | 0,302 | 0,311 | 2,65

## Slide 13: Velocity and pressure U e p – Average over a full rotation step 2 (output)/ step 3 (input)
Since the frozen rotor captures a snapshot of a specific angular position of the fan, another velocity and pressure profile has been considered by averaging all the quantities along the rotation axis
U Profile step3’’ + p profile step3’’
Mag(U) (m/s)
p (Pa)

## Slide 14: Step 3 – Model characteristics
physics setting
Velocity profile and pressure at the suction are imported
Gravity is also included
Pressure reference is set at one corner
Temperature is set at the resistors surface (500 degC), thermal dissipation can occur at the door

## Slide 15: Results - Step 3 – Simplified simulation Averaged over full rotation
Forno 0611 privato degli elementi superflui e delle ventole, profili mediati.
Mag(U) (m/s)
OVEN DOOR: wall + thermal dissipation
RESISTORS: wall + thermal source
PRESSURE POINT CONSTRAIN: pstat = 0 Pa
weakly compressible fluid
Turbolence model: k-ε
ω = 2000 rpm
OVEN WALLS: wall + thermal insulator
CYLINDRICAL FAN: inlet (U profile from step 2 with average along the rotation axis)
FAN FACES:
outlet (profile pstat from step 2 with average along the rotation axis)

## Slide 16: Results – Velocity profile – step1 vs step2
We can compare the results in terms of magnitude of field velocity along the lateral surface of the cylinder that defines the frozen rotor domain
Step 2 (output) /Step 3 (input)
Mag(U) (m/s)
Step 1
Velocity gradient toward the bottom of the fan is captured by both the models.

## Slide 17: Profilo velocità – step1 vs step2
Component u (m/s) along the external cylinder of the fan
Step2
Step1 bottom fan
Step1 top fan
Area
Velocity (m/s)
Area
Area
25
- 25
0
5
10
15
20
-5
-10
-15
-20
25
- 25
0
5
10
15
20
-5
-10
-15
-20
25
- 25
0
5
10
15
20
-5
-10
-15
-20
X (u)
Y (v)
Z (w)

## Slide 18: Profilo velocità – step1 vs step2
Step 2
Step 1 bottom fan
Step 1 top fan
Component v (m/s) along the external cylinder of the fan
7
-1
1
3
5
-3
-5
-7
7
-1
1
3
5
-3
-5
-7
7
-1
1
3
5
-3
-5
-7
Area
Area
Area
Velocity (m/s)
X (u)
Y (v)
Z (w)
Slightly different results here
(Turbolent components along the suction axis)

## Slide 19: Profilo velocità – step1 vs step2
Componente w (m/s) lungo il cilindro circoscritto alla ventola.
Step 2
Step 1 bottom fan
Step 1 top fan
Velocity (m/s)
Area
Area
Area
X (u)
Y (v)
Z (w)
25
- 25
0
5
10
15
20
-5
-10
-15
-20
25
- 25
0
5
10
15
20
-5
-10
-15
-20
25
- 25
0
5
10
15
20
-5
-10
-15
-20

## Slide 20: General overview – step1 vs step3
Velocity magnitude over different tray level positions
Step 3
Step 1
Mag(U) (m/s)

## Slide 21: Results Tray 1 position – step 1 vs step 3
Mag(U) hystogram at h = 0,1 m from the bottom.
Step 3
Step 1
Mag(U) (m/s)
Area
Velocity (m/s)
0
3
2
-1
4
5
6
7
8
9
0
3
2
-1
4
5
6
7
8
9

## Slide 22
Step 3
Step 1
Mag(U) (m/s)
Mag(U) hystogram at h = 0,2 m from the bottom.
22
0
3
2
-1
4
5
6
7
8
9
0
3
2
-1
4
5
6
7
8
9
Results Tray 2 position – step 1 vs step 3
Velocity (m/s)

## Slide 23: Results Tray 3 position – step 1 vs step 3
Step 3
Step 1
Mag(U) (m/s)
Velocity (m/s)
Mag(U) hystogram at h = 0,3 m from the bottom.
23
0
3
2
-1
4
5
6
7
8
9
0
3
2
-1
4
5
6
7
8
9
Area

## Slide 24
Step 3
Step 1
Mag(U) (m/s)
Mag(U) hystogram at h = 0,4 m from the bottom.
Area
Results Tray 4 position – step 1 vs step 3
Area
Velocity (m/s)
0
3
2
-1
4
5
6
7
8
9
0
3
2
-1
4
5
6
7
8
9

## Slide 25: Results Tray 5 position – step 1 vs step 3
Step 3
Step 1
Mag(U) (m/s)
Mag(U) hystogram at h = 0,5 m from the bottom.
Area
Velocity (m/s)
0
3
2
-1
4
5
6
7
8
9
0
3
2
-1
4
5
6
7
8
9

## Slide 26: Results Comparison step 1 vs step 3
Let’s consider how off are the mean values for each tray position between the two steps given the previous hystograms
Tray | shift 1-3 (%)
1 | 6,45
2 | 5,48
3 | 5,60
4 | 3,03
5 | 2,30
average | 4,57

## Slide 27: Final considerations
The numerical model has been experimentally validated for step 2 and deviation from the experimental values ​​can be considered good.
The average deviation of the speed distribution in the trays between step 1 and step 3 is less than 5% at all the levels.
Qualitatively, the velocity profiles between step 1 and step 2 are very similar, and the main difference is due to loss of some turobent components at the outlet of the fan along the suction axis.

## Slide 28: Conclusion
A good balance between accuracy and computational performances can be achieved by studing the fan alone and then imposing velocity profile and pressure
A better usage of the modules can be achieved differentiating the analysis in different steps as presented