## Slide 1: BI Dry 3.0 – A COMSOL® App for Simulating Concrete Drying
D. Ericsson1, J. Carlswärd2, M. Emborg2, M. Westerholm3, M. Åhs4
1 Deflexional, Täby, Sweden 2 Heidelberg Materials Betong, Stockholm, Sweden 3 Heidelberg Materials Cement, Stockholm, Sweden 4 Lund University, Lund, Sweden

## Slide 2: Contents
Introduction
Graphical User Interface
Setting Up a Model
Graphics
Results
Preferences
Underlying COMSOL Model
Access to Specific Functionality
Conclusions

## Slide 3: Introduction
Background and benefits of the software

## Slide 4: Concrete Drying
Moisture enhances concrete curing, but fast drying and low relative humidity (RH) are essential for flooring to prevent deterioration of flooring adhesive
Drying is slow and can delay construction, resulting in premature floor installation and costly testing, disputes, or repairs
Factors like temperature, wind, rain, construction type, and dimensions affect drying rates

## Slide 5: Simulating Concrete Drying
An effective way to predict concrete drying is through finite element-based simulations
Setting up a finite element model requires expertise, but the process is simplified with a compiled COMSOL® app
  Any contractor can leverage the power of COMSOL Multiphysics®
By using simulations, contractors can choose the optimal concrete mix, minimizing environmental impact and reduce costs

## Slide 6: Reductions & Savings
CO2 Emission Reductions
  Decrease the amount of binder
  Use lower-grade concrete where applicable
  Incorporate binder combinations with slag, fly ash and other additions
  Select an optimal design
Cost Savings
  Accelerate construction timelines
  Prevent costly failures

## Slide 7: Background
Longstanding Expertise For decades, Heidelberg Materials has offered customers finite element-based software solutions
Launch of HETT22 in 2022 [1] A COMSOL Multiphysics®-based tool, HETT22 was developed to simulate early-age temperature and strength development
Development of BI Dry 3.0 Following the success of HETT22, Heidelberg Materials chose the same platform to support BI Dry 3.0, a software focused on simulating concrete drying
1. D. Ericsson et al., COMSOL Conference 2023 Munich www.comsol.com/paper/hett22-a-comsol-app-to-accurately-simulate-plan-and-monitor-concrete-castings-122611

## Slide 8: Differences between HETT22 and BI Dry
Timescale While HETT22 and BI Dry share similarities, concrete drying in BI Dry spans months or years, unlike the shorter timescale of hours or days required for early-age strength development in HETT22.
Modeling Both HETT22 and BI Dry utilize the Maturity Method and the heat transfer equation. Additionally, BI Dry solves a convection-diffusion equation for moisture content, which is coupled with heat transfer.

## Slide 9: Joint Efforts
Collaborative Development of HETT22 Created through a partnership between Deflexional AB, a COMSOL Certified Consultant, and Heidelberg Materials
BI Dry 3.0 Development Team Deflexional worked closely with concrete drying experts from Lund University and Heidelberg Materials
Project Success The achievements of this project underscore the essential contributions and collaboration from all involved parties

## Slide 10: Graphical User Interface
An intuitive interface enables contractors to perform advanced simulations with ease

## Slide 11
Select construction scenario to start a new project

## Slide 12
File Menu
Menu
Ribbon
Settings
Status
Graphics

## Slide 13: Ribbon
Create a new project, open, and save
Visualize geometry, mesh, graphs, 2D plots, and 3D plots
Microsoft® Word® and
Microsoft® PowerPoint® reports
Compute
Results as numerical data
Standard libraries and user libraries
Settings

## Slide 14: File Menu
Check for new versions
License information

## Slide 15: Setting Up a Model
Follow the left menu step-by-step from start to finish

## Slide 16: New Project
Select the construction scenario

## Slide 17: Menu
Construction
Change dimensions and materials

## Slide 18: Menu
Construction
Visualization in 3D of the construction and the materials

## Slide 19: Menu
Concrete
Set the concrete type and the casting temperature
Define drying requirements

## Slide 20: Menu
Time
Set dates for the different events
The time between the casting and the simulation time after flooring will be the total simulation time

## Slide 21: Menu
Weather Condition
Temperature, wind, and RH comes from the ASHRAE 2021 database
Precipitation days per month must be set manually for locations outside of Sweden
For Sweden, precipitation data is sourced from SMHI

## Slide 22: Menu
The Location Library makes it easy to re-use data for construction sites
Weather Condition

## Slide 23: Menu
Enter the coordinates for Teatro del Maggio Musicale Fiorentino
Show Location on Map opens Google Maps
Save Location opens a new dialog to save the location:
Weather Condition

## Slide 24: Menu
Locations are saved to the library
Weather Condition

## Slide 25: Menu
Cover of different materials can be added
Time for on/off condition
Cover

## Slide 26: Menu
Pipes with fluid can cool or heat the concrete
Pipe

## Slide 27: Menu
Can include several pipe series with different properties
The pipe medium can be altered
Pipe

## Slide 28: Menu
2D visualization provides an easy-to-use interface for geometric dimensioning
Pipe

## Slide 29: Menu
Heating cables can be arranged in a manner similar to pipe installation
Heating Cable

## Slide 30: Menu
Add measurements to compare simulations with on-site sensor data
Capable of handling large datasets efficiently
Accepts local user settings in a comma-delimited format
Measurements

## Slide 31: Menu
Enables the visualization of output data at selected points
The y-coordinate for the equivalent depth is fixed and cannot be edited, as it depends on the construction type
The x-coordinate is crucial when using pipes or heating cables
Point Probes

## Slide 32: Menu
Notifications and warnings
Date when drying requirement is met
Results

## Slide 33: Graphics
Results visualization

## Slide 34: Graphics
Graph Menu

## Slide 35: Graphics
Graph - Relative Humidity
Weatherproof
Cover removed

## Slide 36: Graphics
Graph - Temperature
Controlled climate
Select graphs

## Slide 37: Graphics
Profile Depth Menu

## Slide 38: Graphics
Profile Depth – Relative Humidity
Drag slider to change time step
x
y

## Slide 39: Graphics
Colormap Menu

## Slide 40: Graphics
Colormap – Relative Humidity
Drag slider to change time step
Set dynamic or static colormap scale

## Slide 41: Graphics
Time Development Menu

## Slide 42: Graphics
The z-coordinate represent time (days)
Time Development - Temperature

## Slide 43: Results
Compare data and create reports

## Slide 44: Compare
Each time a solution is computed, relevant data is saved, allowing for easy comparison of different inputs and outputs
Solutions can be renamed and sections can be filtered
Plots can be updated automatically
Compare and Visualize Different Solutions

## Slide 45: Compare
Visualize
Easy to rename and enable/disable the visualization of different solutions

## Slide 46: Report
Microsoft Word

## Slide 47: Report
Microsoft PowerPoint

## Slide 48: Preferences
Set language, region, appearance, and more

## Slide 49: Preferences
Language can be set to English or Swedish
If the region is set to Sweden, precipitation data averaged from 1991 to 2020 is provided by the Swedish Meteorological and Hydrological Institute (SMHI).
Local Settings

## Slide 50: Preferences
The user can choose between three different themes
Every time BI Dry starts it can check for new versions automatically
Software Updates and Appearance

## Slide 51: Preferences
The number of graphics windows after a calculation can be adjusted from 1 to 4
Each graphics window can have a default plot
For graphs, the default position for the legends can be set
Visualizations and Graphs

## Slide 52: Underlying COMSOL Model
Combining the Model Builder with methods

## Slide 53: Geometry
The 2D geometry is dynamically generated in the Application Builder using methods tailored to the selected construction case
A secondary 3D component is used to visualize the construction with material colors

## Slide 54: Mesh
The mesh automatically adjusts to the selected construction scenario.
If pipes or heating cables are included, boundary layer meshing is added automatically
The problem is always solved in 2D, but the mesh has only one element in the x-direction, effectively reducing it to 1D when possible

## Slide 55: Physics Interfaces
Heat Transfer in Solids
  Heat Source
  Heat Flux
  Thin Layer
Stabilized Convection-Diffusion Equation
Domain ODEs and DAEs
  Calculate the equivalent time (maturity)
Events
  Efficiently manages dynamic changes in the model such as formwork removal, cover additions, or the activation/deactivation of heating cables or pipes

## Slide 56: Solver Settings
The solver uses MUMPS
The time stepping method is set to BDF
The app users can control
  High solver resolution form the start until a certain amount of days
  The solver step size for the high resolution

## Slide 57: Access to Specific Functionality
A portion allocated for advanced users and researchers

## Slide 58: Preferences
The Concrete User Library enables researchers to add their own concrete mixes
Requires a license key which is bound to the MAC address
Concrete User Library

## Slide 59: License Keys
The Deflexional License Manager manages license key generation and integration with the COMSOL App
Can be tested for free at: deflexional.com/license-manager

## Slide 62: Conclusions
Contractors can now use the latest technology to simulate drying of concrete

## Slide 63: Conclusions
Given the success of HETT22, BI Dry 3.0 has been completely rebuilt on the same platform utilizing COMSOL Multiphysics® and COMSOL Compiler™.
BI Dry 3.0 uses the Maturity Method and the heat transfer equation plus a convection-diffusion equation for moisture content, coupled with heat transfer.
By using simulations, significant cost savings and environmental benefits can be realized by choosing the right concrete and construction under certain conditions.
BI Dry 3.0 is scheduled for release before the end of 2024.
Any contractor can now leverage the power of COMSOL Multiphysics® to simulate the drying of concrete.

## Slide 64
We maximize the benefits of
engineering simulations
Daniel Ericsson
CEO & Founder
daniel.ericsson@deflexional.com Phone: +46-70-586 00 98
www.deflexional.com