## Slide 1
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
Aurélien Lejeune (Ph.D., President)
+33 (0)7 86 53 03 85, aurelien.lejeune@protostep.fr
PROTOSTEP, Cergy-Pontoise, 95015, France

## Slide 2
About PROTOSTEP
Simulation, Expertise, R&D solutions
French company founded in 2019
PROTOSTEP, SAS
32, Boulevard du Port, CS20001, 95015, Cergy-Pontoise
Headquarters in La Turbine (95015, Cergy-Pontoise)
Main premisses in Paris-Saclay campus (91120, Palaiseau)
2 Doctors with Ph.D. in Physics
1 Engineer in Electrotechnics
Expertises:
Fundamental Physics
Plasma Physics
CFD, turbulence and shock wave
On-going developments:
Neural Networks based methods
Fields of application:
DC/RF/microwave plasmas
Wind/water fluid-structure interactions
EM/High-voltage environnements
Structural mechanics and Fatigue
Heat transfers
Missions:
Expertise and Consultancy
Numerical modelling and Study
Standalone Application

## Slide 3
Plasma, the fourth state of matter
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  Rare on Earth at the natural state: aurora borealis, lightning, flame
  Most abundant form of ordinary matter in the Universe: stars, intracluster medium, intergalactic medium
  Plasma contains electrons, ions and neutrals (atoms and molecules)
  Plasma can be artificially generated over a wide range of operating conditions: Low-pressure plasma, Atmospheric-pressure plasma, DC discharge, Arc discharge, RF/microwave plasma, …
  3 categories of plasma:
    Cold plasmas (low pressure < 1 mbar, ambient temperature ~300 K)
    Thermal plasmas (atmospheric pressure, medium temperature ~103-4 K)
    Fusion plasmas (high pressure ≥ 1 atm, high temperature ~106 K)
The more the particle interactions increase, the more the challenges in simulation are met

## Slide 4
Problem statement
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
[1] M. Moisan and J. Pelletier, Physique des Plasmas Collisionnels - Application aux décharges haute fréquence, EDP Sciences, 2006
[2] B. Hrycak, M. Jasinski and J. Mizeraczyk, Tuning characteristics of cylindrical microwave plasma source operated with argon, nitrogen and methane at atmospheric pressure, PRZEGLĄD ELEKTROTECHNICZNY (Electrical Review), ISSN 0033-2097, R. 88 NR 6/2012
  Microwave plasmas (0.3-300GHz) are used in industry for various applications such as in microelectronics or decomposition of greenhouse gases
  High-pressure microwave plasmas are still studied in laboratories since they are experimentally characterized by specific phenomena of contraction or filamentation [1]
FIGURE 1. Cylindrical microwave plasma source operated with Argon at atmospheric pressure [2].
Ar+
Ar*
e-
Energy source
+
Ar flow
Ar plasma
Ar

## Slide 5
  In-Plane Microwave Plasma - Application ID: 8664
  Inductively Coupled Plasma (ICP) Torch - Application ID: 18125
  Coaxial to Waveguide Coupling - Application ID: 1863
Overview of the existing models
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
RF module + Plasma module
AC/DC module + Plasma module
RF module
→ valid at low pressure, no increase in temperature
→ valid at atmospheric pressure with an increase in temperature, no reaction set is considered, thermodynamic equilibrium vs T is assumed for the gas mixture properties
→ waveguide-to-coaxial coupling is observed, no plasma

## Slide 6
  In that context, a fully-coupled microwave plasma model at atmospheric pressure with COMSOL Multiphysics® is a necessary step to optimize the development of such a plasma reactor
  Four blocks of Physics must be considered to study this problem:
    Electromagnetics for the microwave propagation and plasma interaction – RF module
    Fluid dynamics for the gas mixture flow – CFD module
    Heat transfers for the thermodynamic equilibrium – Heat transfer module
    Plasma physics for the electron and heavy particule production – Plasma module
  The expected results are:
    Production of the plasma
    Absorption of the microwave (skin effect)
    Waveguide-to-coaxial coupling
    Increase in the gas temperature
Main goals and expected results
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes

## Slide 7
  Fluid approach:
    Continuum
    Transport equations
    Assumed Maxwellian EEDF
  Limitations:
    Reduced electric field:
    Electron density:
    Debye length:
    Gas pressure:
Simulation of plasmas: Numerical assumptions [3]
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
(low degree of ionization)
(apparent charge neutrality)
These assumptions are satisfied in the present case study.
[3] J. Crompton and L. Gritter, Plasma modeling in COMSOL Multiphysics®, AltaSim Technologies - https://www.comsol.fr/video/modeling-plasmas-in-comsol-multiphysics

## Slide 8
  Electron density transport [4]:
Simulation of plasmas
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
Net electron production [5]
Maxwellian EEDF [1]
Convection of electrons due to fluid motion (u) is neglected
E is the electric field driven by the Maxwell’s equations
[1/(m3.s)]
[1/(m2.s)]
This is how electron density balance is computed.
[4] COMSOL Help Resources: Plasma Module > User's Guide > Plasma Interfaces > Plasma Reactors Theory
[5] W. Zhang, Recherche numérique et expérimentale sur les propriétés de décharge et les caractéristiques de propagation électromagnétique dans les torches à plasma micro-ondes, Toulouse INP, 2019

## Slide 9
  Electron energy density transport [6]:
Simulation of plasmas
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
Electron energy transfers [5]
Convection of electrons due to fluid motion (u) is neglected
E is the electric field driven by the Maxwell’s equations
Q is an external heat source driven by the Electron heat source
Heat source for the electrons
(absorbed power density [1])
[W/m3]
[W/m2]
This is how microwave power is transferred to the electrons.
[6] COMSOL Help Resources: Plasma Module > User's Guide > The Drift Diffusion Interface > Theory for the Drift Diffusion Interface > Electron Transport Theory

## Slide 10
  Heavy species mass fraction transport [7]:
Simulation of plasmas
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
[kg/(m3.s)]
[kg/(m2.s)]
[7] COMSOL Help Resources: Plasma Module > User's Guide > The Heavy Species Transport Interface > Theory for the Heavy Species Transport Interface > Multicomponent Diffusion Equations
This is how heavy species mass fraction balance is computed.
[5]

## Slide 11
Simulation of plasmas
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
This is how reactions in a plasma heat the background gas.
[8] Plasma Module > User's Guide > The Heavy Species Transport Interface > Theory for the Heavy Species Transport Interface > Thermodynamic Properties
[9] E. Goos, A. Burcat and B. Ruscic, “EXTENDED THIRD MILLENIUM IDEAL GAS AND CONDENSED PHASE THERMOCHEMICAL DATABASE,” [Online]. Available: http://garfield.chem.elte.hu/Burcat/THERM.DAT
  Thermodynamic properties: Total heat source for heavy species [8]
Enthalpy of reaction in J/mol from the NASA polynomials [9]
[W/m3]
  Poisson’s equation [4]
Space charge density
This is how plasmas react with an external electric field.
Im(εr) → Absorption is expected in the plasma

## Slide 12
Simulation of electromagnetic wave propagation
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  Wave equation:
    In a rectangular waveguide:
TE10 mode is expected in the rectangular waveguide
Magnetic field is not considered here since its interaction with the electrons can be neglected (non-magnetized plasma)
This is how EM field propagation is computed.

## Slide 13
Simulation of heat transfers
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  Heat equation:
[W/m3]
k is the thermal conductivity in W/m/K
Cp is the heat capacity in J/K/kg
Heat capacity in J/mol/K from the NASA polynomials [9]
This is how thermal equilibrium is computed.

## Slide 14
Simulation of fluid dynamics
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  Navier-Stokes equation:
This is how fluid flow is computed.
[N/m3]

## Slide 15
Experimental set-up (2D model)
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
WR975 rectangular waveguide
Cylindrical plasma
2D Model design

## Slide 16
Results: Waveguide-to-coaxial coupling
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
TE10
TE10
TE10
TEM
TEM
w/o plasma
with plasma

## Slide 17
Results: Wave absorption and skin effect
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
with plasma
Skin effect
Wave absorption

## Slide 18
Results: Gas mixture temperature
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
Wave heating
with plasma

## Slide 19
Results: Gas mixture flow velocity
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
The change of the thermodynamic and fluid properties of the gas mixture with the gas temperature may affect the flow velocity.
with plasma

## Slide 20
Conclusions
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  A fully-coupled microwave plasma model at atmospheric pressure has been successfully achieved in Ar with COMSOL Multiphysics®
  Waveguide-to-coaxial coupling has been recovered in the presence of a cylindrical plasma crossing a rectangular waveguide as expected from the theory of the transmission lines
  Skin effect has been observed as expected from the high-pressure plasma theory
  A rise of the gas mixture temperature has been observed according the thermodynamic properties and the wave-heating due to the electrons in a resistive plasma

## Slide 21
Next steps
Atmospheric Plasma Modelling Applied For Thermal Plasma Assisted Processes
  Next works will focus on:
    The EEDF’s when they are computed from the Boltzmann equation
    The operating conditions and design
    The gas flow regime at higher mass flow rates
    Other feed gases with more by-products
    Heavy-heavy particle collisions
    Radiative heat transfers
Thank you for your attention