## Slide 1
J. McKenna1, J. Karst2, J. Luttrell IV1, R. Riedel1, S. Kar3, and P. Duff4
1. Roger F. Wicker Center for Ocean Enterprise, The University of Southern Mississippi Gulfport, MS, USA 2. CTI, Columbus, OH, USA
3. RENCI, Chapel Hill, NC, USA
4. Naval Research Laboratory, Bay St. Louis, MS, USA
4 October 2024
Potential Fields Modeling to Support Machine Learning Applications in Maritime Environments

## Slide 2: Port of Gulfport, Gulfport MS
The Roger F. Wicker Center for Ocean Enterprise is Located at the Port and is comprised of two buildings on Port property: The Marine Research Center (MRC), and the Roger F. Wicker Ocean Enterprise Facility (Wicker Building or OEF)

## Slide 3: Motivation
Unmanned Underwater Vehicles (UUVs) equipped with magnetic sensors are crucial for detecting ferromagnetic objects underwater. Accurate modeling of the magnetic and gravitational field interactions in these environments ensures the effectiveness of detection operations.
Numerical modeling potential fields in maritime settings is important
  UXO
  Archeological Items (e.g. shipwrecks)
  Geological features
Field experiments are complex
Data collection areas are cluttered
Calibrated simulations are ideal to generate quality training data to develop ATRs using AI/ML techniques
Multiphysics modeling can be important (magnetic/gravity/acoustics)

## Slide 4: UUV SideScan Testing in Shallow Harbor

## Slide 5: UUV SideScan Testing in Shallow Harbor

## Slide 6: Background Theory

## Slide 7: First Order Modeling: Earth’s Magnetic Field Induces the Observed Anomaly
N
E
Z
Pipe azimuth
Pipe dip
N
E
Z
Magnetic declination
Magnetic inclination
Angles needed to calculate the perpendicular and parallel components of B0

## Slide 8
For assumed relative permeability 2, 5, 50, 100, 200, 500, corresponding susceptibility k would be 1, 4, 99, 199, and 499
For the direction perpendicular to the pipe, the effective susceptibility is given below with N being the self-demag factor (N=1)
Along the pipe length, the self-demag factor is approximately 0
For the first order modeling, we do the following:
  Calculate the pipe volume, and equivalent spherical radius
  Project the inducing field to two components: (1) perpendicular to the pipe and parallel to the pipe
  Obtain the magnetization for both directions:
  Calculate the responses by using a sphere with the above magnetization and equivalent volume of the pipe
First Order Modeling: Earth’s Magnetic Field Induces the Observed Anomaly

## Slide 9: Frist Order Modeling: Earth’s Magnetic Field Induces the Observed Anomaly
Assumptions: large stand-off distance (~5x target size)
Approximations: dipole representation
Inputs: calculated dipole moment
Outputs: magnetic anomaly

## Slide 10: Field Data

## Slide 11: USV/UUV Platforms
Fused Sensor Data
Magnetics
IMU Gyro
(roll, pitch, yaw)
IMU Accel
(x, y, z)
GPS + RTK
IMU Mag
(x, y, z)
IMU

## Slide 12: USV Orientation Correction
The uncorrected data in the top subplot has dramatic changes due to the circular course of the vehicle in this test.
After orientation correction, the second subplot shows a dramatically reduced variation in magnetic field due to the background environment. Note that onboard IMU data at a low sample rate was used for these corrections, and a higher quality source of orientation data would reduce these effects even further.
This orientation corrected data is more suitable for analysis to detect small magnetic changes indicative of a target of interest.

## Slide 13: USV Shallow Harbor Data

## Slide 14: Magnetic Testing
Pipe Parallel / Orthogonal
Pipe Vertical

## Slide 15: USV: Cylindrical Magnet
Z
X
Y
The plots at right show the observed vs simulation model results for an 8" long 1" diameter cylindrical magnet.The model uses the GPS path of the test platform, and target properties as input
The sensor array travels along a West-Northwest direction (X is Easting, Y is Northing, Z is Vertical)
The simulation matches the observed data within measurement accuracy for all four test passes for both the total field and vector components.

## Slide 16: USV: 12" Vertical Pipe
Z
X
Y
The plots at right show the observed vs simulation model results for a 12" long ~4.5" diameter steel pipe. The model uses the GPS path of the test platform, and target properties as input
The simulation matches the observed data within measurement accuracy for all four test passes for both the total field and vector components. The background noise in this dataset is comparatively higher due to the lower amplitude of the pipe signature vs the magnet.

## Slide 17: COMSOL Simulations

## Slide 18: Parameters
Name | Expression | Value | Description
mur_pipe | 100 | 100 | Relative permeability
H0 | 46353.6[nT] | 4.6354E−5 T | Geomagnetic field
Incl | 58.77291[deg] | 1.0258 rad | Local inclination
Decl | -4.28[deg] | −0.0747 rad | Local declination
xx0 | 12[in] | 0.3048 m | Length of pipe
xx | 24[in] | 0.6096 m | Length of pipe
xxx | 36[in] | 0.9144 m | Length of pipe
pir | 4.026 [in] | 0.10226 m | Inner radius of pipe
por | 4.5[in] | 0.1143 m | Outer radius of pipe

## Slide 19: Variables

## Slide 20: Variables
Name | Expression | Description
Gx | cos(Incl)*sin(Decl) | Geomagnetic field direction, x-component
Gy | cos(Incl)*cos(Decl) | Geomagnetic field direction, y-component
Gz | -sin(Incl) | Geomagnetic field direction, z-component

## Slide 21: Component

## Slide 22: Geometry
Geometry 1
Geometry statistics | 
Description | Value
Space dimension | 3
Number of domains | 10
Number of boundaries | 84
Number of edges | 156
Number of vertices | 92

## Slide 23: Materials

## Slide 24: Background Material
Background Material
Material parameters |  |  | 
Name | Value | Unit | Property group
Relative permeability | 1 | 1 | Basic
Basic | 
Description | Value
Relative permeability | 1

## Slide 25: Pipe
12” Pipe
Material parameters |  |  | 
Name | Value | Unit | Property group
Relative permeability | mur_pipe | 1 | Basic
Basic | 
Description | Value
Relative permeability | mur_pipe
24” Pipe
36” Pipe

## Slide 26: Magnetic Fields, No Currents
Magnetic Fields, No Currents
Settings |  | 
Description | Value | Unit
Solve for | Reduced field | 
Background magnetic field, x-component | H0*Gx/mu0_const | A/m
Background magnetic field, y-component | H0*Gy/mu0_const | A/m
Background magnetic field, z-component | H0*Gz/mu0_const | A/m

## Slide 27: Mesh 1
Mesh
Mesh statistics | 
Description | Value
Status | Complete mesh
Mesh vertices | 396865
Tetrahedra | 2328593
Triangles | 50614
Edge elements | 1868
Vertex elements | 92
Number of elements | 2328593

## Slide 28: Study
Computation information | 
Computation time | 2 min 37 s

## Slide 29: Model Simulations

## Slide 30: Cut Line Parallel to UUV: 1m Above
Dataset: Cut Line Parallel to UUV: 1m Above
Line data | 
Description | Value
Line entry method | Two points
Points | {{50, 0, 6.8}, {50, 100, 6.8}}
Bounded by points | Off
Additional parallel lines | On
Distances | {50, 100}
Orthogonal vector | {1, 0, 0}

## Slide 31: 1m Above UUV Parallel to Path: B
Mag Flux Density Norm (nT)

## Slide 32: 3m Above UUV Parallel to Path: B
Mag Flux Density Norm (nT)

## Slide 33: 5m Above UUV Parallel to Path: B
Mag Flux Density Norm (nT)

## Slide 34: 1m Above UUV Parallel to Path: By
Mag Flux Density Norm: By (nT)

## Slide 35: 1m Above UUV Parallel to Path: Bz
Mag Flux Density Norm: Bz (nT)

## Slide 36: ML Overview
Purpose: Use simulated magnetic sensor data to predict anomaly signatures
Approach: Four machine learning models for confirming findings
Results: Labeled simulated vs predicted sensor measurements

## Slide 37: Machine Learning (ML) Background
An algorithm that "learns" from repetitive tasks
Based on models with several thousand parameters
Parameters are estimated using optimization
Models need large amounts of data to converge
Many models tend to be "black-box", not explainable inner-workings

## Slide 38: ML Modeling
Regression: ML model based on multiple regression
Boosting: ML model based on tree ensembles
DNN (Deep Neural Network): ML model based on neuron layers (relies on present state only)
LSTM (Long Short-Term Memory): ML model based on present and past (remembered) states

## Slide 39: ML Approach
Regression
  Trained as above for DNN:
    Training data was simulated from a modeled 12-inch isopipe (100 permeability)
    Testing data was simulated from a modeled 24-inch isopipe (100 permeability)
    Used to predict the total field (magnetic flux density norm) measurements that a sensor would see in the field
General regression model:
y = β0+β1X1+β2X2+…+βnXn+e, where
y is the dependent variable, β0 is the intercept, β are coefficients, X are the predictors, and e is the independent and identically distributed error term.

## Slide 40: ML Approach
Boosting
  Dichotomized sensor readings to above and below mean absolute value
  Used target permeability, aspect ratio, and UUV speed as predictors
  Used grid-search to find best values for tree number and maximum depth

## Slide 41: ML Approach
DNN
  Trained on the simulated vector components of the B field.
    Training data was simulated from a modeled 12-inch isopipe (100 permeability)
    Testing data was simulated from a modeled 24-inch isopipe (100 permeability)
    Used to predict the total field (magnetic flux density norm) measurements that a sensor would see in the field

## Slide 42: ML Approach
Long Short-Term Memory (LSTM)
  Trained on the simulated vector components of the B field.
  Ran model for total-, x-, y-, and z-fields
  Used a sequence of 10 past data points to predict current point
  Iterated over entire data set

## Slide 43: ML Results
Regression
  Best fit (top figure)
  R-squared 0.98
DNN
  Good fit, may need to increase data size (bottom figure)

## Slide 44: ML Results
LSTM
  Good fit (figure to the right)
Boosting feature importance (%)
  Target permeability (0.44)
  Target aspect ratio (0.30)
  UUV speed (0.26)

## Slide 45: Conclusions & Way Ahead
Simulations in data-scarce situations are essential
Relatively simple ML models are able to reproduce simple target signatures for a variety of magnetic properties and geometries
Once a base model is validated is straightforward to generate more data for certain ML approaches
Next steps:
    Add Acoustics/Gravity Physics
    Deploy Apps internally for ML training using COMSOL Server
    Perform Uncertainty Quantification/Optimization

## Slide 46: Simple COMSOL APP

## Slide 47
Questions?
jason.mckenna@usm.edu