## Slide 1: 3D Ultrasonic Simulations for Pulse Echo and Pitch Catch Testing
Haiqi Wen
Lead Scientist @ Baker Hughes

## Slide 2: Oil and Gas Production Process
Upstream
Midstream
Downstream
Exploration: Locating potential sites for oil and gas drilling and extraction
Drilling: Boring a hole using a drill bit to create a well for oil and natural gas production
Extraction: Oil and natural gas flows up from the well bore and fracturing fluid is then recovered .
Processing: Oil and natural gas are separated, then transferred to the gas processing plants.
Storing: Natural gases are usually stored in underground spaces such as depleted reservoirs, while finished oil products, crude oil and refined oil commonly use above ground tanks as storage.
Transportation: Unrefined oil is transported via tankers and pipelines, while final petroleum products travel to the market through trucks, railroad cars, etc…
Refining: Converting oil and natural gas into petroleum products that can be used for various purpose.
Distribution: The finished petroleum products are distributed to business and consumers.

## Slide 3: Cement Bonding Evaluation
Well cementing is a key procedure during well construction, The cement sheath provides a hydraulic seal that prevents fluid communication between producing zones in the borehole and blocking the escape of fluids to the surface.
Cement-bonding logs (CBL) and variable-density log (VDL) leverage ultrasonic tools run on wireline to provide highly reliable estimates of well integrity and zone isolation.
Fang et al. 2022

## Slide 4: Piezoelectric Transducer Modeling
Matching Layer
Damping Material
Piezoelectric Material
Absorbing Layer
Fluid
Transducer Housing
In this study, four physics modules are introduced to the Multiphysics model:
Electrostatics module (es) is coupled to the Elastic Waves, Time Explicit (elte) module to transform voltage signal to elastic wave.
Elastic Waves, Time Explicit (elte) module is coupled to Pressure Acoustics, Time Explicit (pate) module to model fluid-structural interaction at the transducer’s boundary.
An external electrical circuit is coupled to the terminal of the piezoelectric element.

## Slide 5: Boundary Conditions
Absorbing layer is introduced to absorb acoustic waves and prevent reflection
1/8
1/4
1/2
Full Model
Only 1/8 of the model is simulated to improve computation efficiency. Full model response can be obtained by creating mirror data sets.

## Slide 6: Transducer Dimension and Mesh Setting
Thickness of the piezoelectric transducer is set to of the wavelength, the thickness of the matching layer is set to of the wavelength.
In this study, a dG time-explicit method is used to solve the system. The default for Elastic Waves interface is to use quartic shape functions. The maximum element size is defined as
Mesh size does not to be continuous at interface
Mesh size is continuous at interface

## Slide 7: 2D Axisymmetric Model vs 3D Model
2D Axisymmetric Model
3D Model
F0 = 280 kHz
3D model results were obtained by evaluating the pressure response at the yz-cut plane (x = 0)

## Slide 8: Model Validation
Peak Pressure
Transducer’s center frequency is at 280 kHz
Amplitude is normalized.
Simulation and measurement data agrees well at near field. The maximum pressure is found on axis.
Side lobes were observed in measurement data, whereas the model results does not exhibit side lobe.
Local cancellation are found in simulation, while the experiment data shows a continuous decay.

## Slide 9: Pulse Echo Simulation
7 in casing (0.5 in thickness)
Fluid
Transducer
Pressure Waveform
Pressure Probe
Modified Square Pulse Signal
Wave Propagation
Pulse-echo is an ultrasonic non-destructive testing (NDT) technique using ultrasonic pulsed waves to find defects in materials.

## Slide 10: Estimate Casing Thickness
Extract Waveform Envelope using Hilbert Transform

## Slide 11: Pitch Catch Simulation
Primary A0
Primary A0 arrival
Casing A0 leaking into water
SecondaryA0
Secondary A0 arrival
Casing A0
Secondary S0
Fluid mode
Primary S0 arrival
Unlike the pulse-echo testing, where the same transducer is used to send and receive the signal. In pitch-catch testing, a transmitter and one or multiple receiver are used to send and receive the signal

## Slide 12: Simulations vs. TOC Fixture Measurements. Waveforms
12
Expt.
Sim.
Primary A0
Secondary A0
Tertiary A0
Fluid Mode
Quat. A0
Free Pipe
Primary A0
Secondary A0
Tertiary A0
Quat. A0
Fluid Mode

## Slide 13: Summary
In this study, ultrasonic piezoelectric transducers are coupled to the fluid to study acoustic wave propagation in pulse-echo and pitch catch simulation.
The model can be used to characterize transducer’s free field response, estimate casing thickness and provide cement bonding evaluation.
Overall, COMSOL model simulations are capable to capture the experimental response. With good tuning, the model can be used to develop transducers and test setups to reduce prototyping cost.